## Slide 1: Crafting an Automated Door Control System

## Slide 2: LIST OF COMPONENTS:
ESP32 MICROCONTROLLER
SERVO MOTOR(SG90)
ULTRASONIC SENSOR(HC-SR04)
JUMPER WIRES
BREAD BOARD

## Slide 3
CIRCUIT DAIGRAM:
CONNECT TRIG PIN-D5

## Slide 4
CONNECT ECHO PIN -D18

## Slide 5
CONNECT VCC-3.3V

## Slide 6
CONNECT GND-GND

## Slide 7
CONNECT RED WIRE-VIN

## Slide 8
CONNECT BLACK WIRE-GND

## Slide 9
CONNECT YELLOW WIRE-D13

## Slide 10
CODE:
#include <ESP32Servo.h>
Servo myservo;
const int trigPin = 5;
const int echoPin = 18;
const int servoPin = 13;
const int doorOpenAngle = 90;
const int doorCloseAngle = 0;
const int distanceThreshold = 30;
void setup() {
myservo.attach(servoPin);
pinMode(trigPin, OUTPUT);
pinMode(echoPin, INPUT);
Serial.begin(115200);
}
void loop() {
long duration, distance;
digitalWrite(trigPin, LOW);
delayMicroseconds(2);
digitalWrite(trigPin, HIGH);
delayMicroseconds(10);
digitalWrite(trigPin, LOW);
duration = pulseIn(echoPin, HIGH);
distance = duration * 0.034 / 2;
Serial.print("Distance: ");
Serial.print(distance);
Serial.println(" cm");
if (distance <= distanceThreshold) {
Serial.println("Obstacle detected, opening door!");
myservo.write(doorOpenAngle);
} else {
Serial.println("No obstacle, closing door!");
myservo.write(doorCloseAngle);
}
delay(1000);
}
CONTINUE

## Slide 11
STEP 1
Copy code paste in Arduino new Sketch

## Slide 12
STEP 2
Board---->esp32---->esp32-wroom-DA module

## Slide 13
STEP 3
Tools---->port---->select your com

## Slide 14
board name automatically change to dark

## Slide 15
1.Compile the code
2.After Compilation build the code to board

## Slide 16
After Build the code the output like this