## Slide 1: Unveiling Analog Input Reading Magic

## Slide 2: LIST OF COMPONENTS:
ESP32 MICROCONTROLLER
POTENTIOMETER
BREAD BOARD
LED
JUMPER WIRES

## Slide 3: CIRCUIT DAIGRAM:
CONNECT GND-GND
VOUT-D34
VCC-VIN

## Slide 4
CONNECT ANODE-D13
CATHODE-GND

## Slide 5: CODE:
#define LED_PIN 13
#define POT_PIN 34
void setup() {
pinMode(LED_PIN, OUTPUT);
pinMode(POT_PIN, INPUT);
Serial.begin(115200);
}
void loop() {
int potValue = analogRead(POT_PIN);
int ledBrightness = map(potValue, 0, 4095, 0, 255);
analogWrite(LED_PIN, ledBrightness);
Serial.print("Potentiometer Value: ");
Serial.print(potValue);
Serial.print(" - LED Brightness: ");
Serial.println(ledBrightness);
delay(1000);
}

## Slide 6
STEP 1:
Copy code paste in Arduino new Sketch

## Slide 7
STEP 2:
Board---->esp32---->esp32-wroom-DA module

## Slide 8
STEP 3:
Tools---->port---->select your com

## Slide 9
board name automatically change to dark

## Slide 10
1.Compile the code
Compilation build the code to board

## Slide 11
OUTPUT:
When we upload the code the LED will adjusted using the potentiometer and we can see the potentiometer and the LED brightness value
After Build the code the output like this