## Slide 1: Crafting a Temperature and Humidity Monitoring System

## Slide 2: LIST OF COMPONENTS:
ESP32 MICROCONTROLLER
DHT11
LCD DISPLAY 16X2 I2C
JUMPER WIRES
BREAD BOARD

## Slide 3
Circuit Diagram:-
3v3 VCC

## Slide 4
D5------->Signal (or) Data

## Slide 5
GND-------->GND

## Slide 6
CONNECT SDA-D21

## Slide 7
CONNECT SCL-D22

## Slide 8
CONNECT VCC=VIN
CONNECT GND-GND

## Slide 9
CODE:
#include <Wire.h>
#include <LiquidCrystal_I2C.h>
#include <DHT.h>
#define DHTPIN 5
#define DHTTYPE DHT11
DHT dht(DHTPIN, DHTTYPE);
LiquidCrystal_I2C lcd(0x27, 16, 2);
void setup() {
Serial.begin(115200);
dht.begin();
lcd.init();
lcd.backlight();
lcd.setCursor(0, 0);
lcd.print("Temperature:");
lcd.setCursor(0, 1);
lcd.print("Humidity:");
}
void loop() {
delay(2000);
float temperature = dht.readTemperature();
float humidity = dht.readHumidity();
Serial.print("Temperature: ");
Serial.print(temperature);
Serial.println(" °C");
Serial.print("Humidity: ");
Serial.print(humidity);
Serial.println(" %");
lcd.setCursor(13, 0);
lcd.print(" ");
lcd.setCursor(13, 0);
lcd.print(temperature);
lcd.setCursor(11, 1);
lcd.print(" ");
lcd.setCursor(11, 1);
lcd.print(humidity);
}
CONTINUE

## Slide 10
Step-1:-
Copy code paste in Arduino new Sketch

## Slide 11
Step-2
Board---->esp32---->esp32-wroom-DA module

## Slide 12
Step-3:-
Tools---->port---->select your com

## Slide 13
board name automatically change to dark

## Slide 14
1.Compile the code
2.After Compilation build the code to board

## Slide 15
After Build the code the output like this