## Slide 1: Sculpting Smart Distance Monitoring

## Slide 2: LIST OF COMPONENTS:
ESP32 MICROCONTROLLER
ULTRASONIC SENSOR(HC-SR04)
BREAD BOARD
JUMPER WIRES

## Slide 3
CIRCUIT DAIGRAM:
CONNECT TRIG PIN-D5

## Slide 4
CONNECT ECHO PIN -D18

## Slide 5
CONNECT VCC-3.3V

## Slide 6
CONNECT GND-GND

## Slide 7
CODE:
#define TRIG_PIN 5
#define ECHO_PIN 18
#define OBSTACLE_DISTANCE 20
void setup() {
Serial.begin(115200);
pinMode(TRIG_PIN, OUTPUT);
pinMode(ECHO_PIN, INPUT);
}
void loop() {
long duration, distance;
digitalWrite(TRIG_PIN, LOW);
delayMicroseconds(2);
digitalWrite(TRIG_PIN, HIGH);
delayMicroseconds(10);
digitalWrite(TRIG_PIN, LOW);
duration = pulseIn(ECHO_PIN, HIGH);
distance = duration * 0.034 / 2;
Serial.print("Distance: ");
Serial.print(distance);
Serial.println(" cm");
if (distance <= OBSTACLE_DISTANCE) {
Serial.println("Obstacle detected!");
}
delay(500);
}

## Slide 8
STEP 1
Copy code paste in Arduino new Sketch

## Slide 9
STEP 2:
Board---->esp32---->esp32-wroom-DA module

## Slide 10
STEP 3:
Tools---->port---->select your com

## Slide 11
board name automatically change to dark

## Slide 12
1.Compile the code
2.After Compilation build the code to board

## Slide 13
After Build the code the output like this